mrprob3
MizzouRisc Assignment 3
All instructions assume the use of MizzouRisc.
(3 points each) Write the assembler instructions to do the following
Place the values 1200H into r1
LOAD L#1200, r1
Assuming that r1’s content is 1200, write the single instruction that places 1206 into r1.
LOAD 6#R1, R1
r3’s content is A, write the instruction that multiplies it by 2 and places the result in r4
STM R3, R4
(3 points each) Assemble the following instructions into MizzouRisc machine language
store	r1, (r14)	915E0000
load 4#r14, r14	8E6E0004

(15 points)For the following Small program respond appropriately to the questions.
1	Org 1000
2	Num1: .DW ABAB ABAB, CDCD CDCD
3	Num2: .DW
4	Org 2000
5	load l#1000, r15
6	load (r15), r1
7	load l#5454, r2
8	load h#1454, r2
9	AND r1,r2,r3
10	Store r3, (8#r15)
11	end: branch(alw) end

Trace the program

Use this table for the trace, there may be more cells than needed.
	r15	r1	r2	3	1008
5	00001000
6		ABABABAB
7			00005454
8			14545454
9				00000000
10					00000000

At the completion of the program
What value is in NZVC _0100_____________
What value is in Num2 ______00000000____
List the memory address values for the first 5 lines 1)1000 2)1000, 1004 3)1008, 4)2000, 5)2000 ____________________________