Assignment 3: Assess IDAK 3D calibration
Seth Ahrenbach

1. Objective

The objective of this lab is to assess whether the IDAK 3D sensor is properly calibrated.

2. Method

The company has provided a theoretical error covariance matrix, which I denote givenCo.

givenCo = [ 1 1 1
        1 2 2
        1 2 3 ].

We have been provided with 100,000 test measurements of a beacon with known coordinates, which I denote actual,

actual = [12.9 130.4 23.5]

We assume the provided test measurements are independent of each other. Our procedure, then, assesses whether the instrument contains bias, and determines whether the theoretical covariance matrix is conservative. That is, the provided theoretical covariance matrix should provide an upper bound on the expected error covariance. Thus, we compute the mean of the measurements, denoted meanM, and the error covariance matrix of the test measurements, denoted as covarM. We check that meanM is roughly equivalent to actual, and whether covarM < givenCo.

3. Results

meanM = [ 12.896 130.398 23.495]

We conclude based on this computed mean that the instrument is free from bias.

covarM = [ 0.99743 0.99910 1.00008
        0.99910 2.00373 2.00845
        1.00008 2.00845 3.01143 ]

To check covarM < givenCo, we compute eig(givenCo .- covarM) =

[-0.0168728
        0.0012327
        0.0030546 ].

This is a potentially troubling result, as the first eigenvalue is slightly negative, indicating that the matrix resulting from the subtraction contains a negative value in the diagonal. This means that covarM may fail to be less than or equal to givenCo. One nuance involved in the operation concerns the potential introduction of error via the computation process itself, wherein the computed eigenvalue may be fluctuating around a mean of 0. In this case, the eigenvalue in question may actually be 0. However, my judgment is that -0.0168728 is not close enough to 0 to justify such a conclusion, though indeed the value seems to be converging on 0. It may be that with more test data, the potential error introduced by computation would vanish, but based on this data set, and this eigenvalue, I judge that the theoretical error covariance matrix givenCo is not sufficiently conservative. I do not know the future applications of the sensor, and it may be the case that two decimal places of unexpected error is catastrophic for some of them.

Attached is the Octave code used to generate my results:

# Assignment 3: Assess the calibration of a 3D sensor
# Seth Kurtenbach

actual = [12.9, 130.4, 23.5];
givenCo = [1,1,1;1,2,2;1,2,3];

fm = fopen("A3-MeasurementData(1).bin");

meas = fread(fm, [3, 100000], "float");
meas = meas';

meanM = mean(meas);
# meanM = 12.896, 130.398, 23.495

errorM = meanM .- actual;

varM = var(meas);

covarM = cov(meas);

eigs = eig(givenCo .- covarM);

# eigs = [ -0.0168728
# 0.0012327
#	0.0030546 ]