Assignment 4: Implement a Filter
Seth Ahrenbach

Description: In this assignment, I use data from A3-MeasurementData.bin to implement a filter, estimating 3D coordinates as measured by the sensor.

Deliverables:

1. First observation mean vector z and sqrt of its covariance R.

z1 = [ 12.7785
        130.0927
        23.5293]

      sqrtm(R) = [ .87112 .38768 .30142
        .38768 1.17254 .68910
        .30142 .68910 1.56022 ]

  However, in initializing my filter, I used the following initial input:

        z0 = [0
        0
        0]

        sqrtm(R) = [ 10^5 0 0
        0 10^5 0
        0 0 10^5 ]
     in order to represent an initial state of complete uncertainty.

2. Final mean x and sqrt of covariance matrix P.

        x = [ 12.896
        130.398
        23.495 ]

     sqrtm(P) = [.0027547 .0012260 .000953160
        .001226 .0037079 .0021791
        .00095316 .0021791 .0049339]
3. Three plots showing innovations in x,y,z with sqrts of respective invariances.

4. Plot of Expected distance (blue) vs Euclidean distance (red)

Code
# Assignment 4: Implement a filter to process 3D sensor observations.
# Seth Kurtenbach

actual = [12.9; 130.4; 23.5];

R = [1,1,1;
     1,2,2;
     1,2,3];

fm = fopen("A3-MeasurementData(1).bin");

meas = fread(fm, [3, 100000], "float");

## Initialized Estimate (x, P) ##
x = [0;0;0];

P = [10^10,0,0;
     0,10^10,0;
     0,0,10^10];

for i = 1:100000
    z = [meas(1,i);meas(2,i);meas(3,i)];
    S = P + R;
    W = P * inv(S);

    innovX(i) = z(1) – x(1);
    innVarX(i) = sqrt(S(1,1));
    innVarXmin(i) = -(innVarX(i));

    innovY(i) = z(2) - x(2);
    innVarY(i) = sqrt(S(2,2));
    innVarYmin(i) = - (innVarY(i));

    innovZ(i) = z(3) - x(3);
    innVarZ(i) = sqrt(S(3,3));
    innVarZmin(i) = - (innVarZ(i));

    euc(i) = norm(x - actual, 2);
    expDist(i) = sqrt(sum(eig(P)));

    P = P - (W * S * W');
    x = x + (W * (z - x));

end